## Slide 1: CS420: Fault Tolerance
Laxmikant V. Kale

## Slide 2: Faults, Errors and Failures
Fault
  The cause of an error (e.g. a bug, stuck bit, alpha particle)
Error
  The part of total state that may lead to a failure (e.g. a bad value)
Failure:
  A transition to incorrect service (an event, e.g. the start of an unplanned service outage, premature job termination)

## Slide 3: Transient, Intermittent, and Permanent Faults
Transient
  Usually uncontrollable, environmentally influenced – cosmic radiation
Intermittent
  Marginal or failing hardware
  Through aging, parameter of a device drifts in value, exceeds built-in margin
  E.g. intermittency of contacts at solder joints, threshold voltage of a MOSFET, etc.
Permanent
  Irreversible physical changes
  Usually cause device to be inoperable
  May be the evolution of intermittent errors, also extreme environmental conditions

## Slide 4: Hard vs. Soft
“Hard” usually refers to a hard stop failure
  ~detectable by the system/application/hardware
“Soft” usually refers to data corruption
  ~undetectable by the system/application/hardware

## Slide 5: Where Do Errors in Supercomputers Come From?
HPC systems of today are extremely complex systems made from hardware and software components that were never designed to work together as one complete system
  Dielectric breakdown and electrical breakdown
  Temperature (extremes and variations)
  Aging
  Manufacturing defects
  Stress
  Extreme conditions
  Voltage fluctuation
  Electro-magnetic interference
  Terrestrial neutrons
  Cosmic radiation
  Alpha particles

## Slide 6: How Do Errors Manifest in Supercomputers?
Hardware or software crashes
  System reboot usually fixes this
  Application usually crashes, must be restarted
Performance variation
  Terribly hard to diagnose and fix
  Usually wasteful but not destructive
  Much worse for tightly-coupled numerical simulations
Data corruption
  Clearly a wrong answer in a calculation – must re-run some of the simulation again
  Silently corrupted calculation – result is corrupted, but in a way that we cannot tell

## Slide 7: Failures on Titan
Failure Category | Failure Type | Count | Percentage
GPU | GPU DBE GPU DPR GPU Bus SXM power off SXM warm temp | 51 66 11 14 2 | 16.1% 20.8% 3.5% 4.4% 0.6%
Processor | Machine check exception bank 0,2,6 | 31 | 9.8%
Memory | Machine check exception Bank 4 MCE | 120 | 37.9%
Blade | Voltage fault Module failed | 12 10 | 3.8% 3.1%

## Slide 8: Typical Fault-Tolerance Problem
Assume:
  A problem that needs to run for a long time (e.g. days) …
  On a system in which the MTBF (Mean Time Between Failures) is relatively small (e.g. hours)
Problem:
  How to get a complete execution ?

## Slide 9: Typical Fault-Tolerance Solution
Checkpoint/Restart
  Explore iterative/periodic pattern in applications
  After running for a given period, checkpoint the application (i.e. save minimal state required to be able to restart, if there is a failure)
Basic Idea:
  Do some work; save/dump state; do more work; save state, do more work, etc., etc.
  In case of failure, restart from last checkpoint taken

## Slide 10: Typical Fault-Tolerance Solution
compute
dump
compute
dump
compute
dump
. . .
compute
dump
comp
restart
compute
dump
. . .
Execution without failures:
compute
Execution with a failure:
Dump (Checkpoint) phase: save essential state
  typically saving data to disk (checkpoint file)
Restart phase: recover essential state

## Slide 11: How Often to Checkpoint?
Tradeoffs in Dump Period Selection:
If T(compute) >> T(dump)
  Less overhead imposed by dumping data
  More work likely to be lost when a failure occurs
If T(compute) ≈ T(dump)
  More overhead due to dumping data
  Less work is lost in case of failure
Classical checkpoint decision:
What is the checkpoint period that will minimize the total application execution time ?
Ref: J.Daly – A higher order estimate of the optimum checkpoint interval for restart dumps. Future Generation Computer Systems, 22(2006), pp.303-312

## Slide 12: Standard Fault-Tolerance Model
A simple model
  : regular computation
  δ: dump of checkpoint
  X: failure, R: recovery time, M: MTBF
  Ts: Total “useful” execution = N 
  Tw: Total walltime of execution

## Slide 13: Standard Fault-Tolerance Model
A simple model (cont.):
Tw() = computation time + dump time + rework time + recovery time
= Ts + (Ts/ – 1)  + [+]  n() + R n()
where:
: fraction of work lost, on average
n(): number of failures, on average

## Slide 14: Standard Fault-Tolerance Model
A simple model:
Assumptions:
  Only one failure per compute segment
  No failures during dump and recovery
Approximations (see reference):
   = ½
  n() ≈ Ts [(+δ)/M] / 
Tw() = Ts + (Ts/ – 1) + [( +)/2 + R] Ts/ (+) / M
To minimize Tw() : d(Tw)/d = 0
  (opt) = [ 2  (M+R)] ½ for (+) << M
Example: M=1 hour, R==1 min.   (opt) ≈ 11 min. , ≈ 9% overhead!
But for checkpoints to disk,  can be 10+ minutes (esp. if almost all memory is being dumped)

## Slide 15: Higher Order Fault-Tolerance Model
Note: (ignore for the exam)
This comes from a simple, first order model
A higher order model (see Ref.):
   (opt) = ( 2 δ M ) ½ – δ if δ  M/2
   (opt) = M if δ  M/2
In practice, checkpoint/restart is largely used by real applications
  Tolerance to failures and to execution scheduling
  Job “failure” = Job is aborted by the system scheduler
  New executions simply restart from last checkpoint
  Dump phase can be accelerated with local disks/filesystems

## Slide 16: Fault Trends in Large Systems
No matter how reliable the components are, a large system will be likely to suffer a failure

## Slide 17: Fault Trends in Large Systems
No matter how reliable the components are, a large system will be likely to suffer a failure

## Slide 18: Fault Tolerance in Parallel Systems
As machines grow in size
  MTBF decreases
  Applications have to tolerate faults
Checkpoint/Restart may not scale
  All nodes are rolled back just because one crashed
  Even nodes independent of the crashed node are restarted
  Typically requires same configuration for restart

## Slide 19: Fault Tolerance References
Checkpoint-based methods
  Coordinated – Blocking [Tamir84], Non-blocking [Chandy85] Co-check, Starfish, Clip – fault tolerant MPI
  Uncoordinated – suffers from rollback propagation
  Communication – [Briatico84], doesn’t scale well
Msg-Log schemes
  Pessimistic – MPICH-V1 and V2, SBML [Johnson87]
  Optimistic – [Strom85] unbounded rollback, complicated recovery
  Causal Logging – [Elnozahy93] Manetho, complicated causality tracking and recovery
  Charm++ based methods : see next slides

## Slide 20: Silent Data Corruption
Cosmic Rays from Outer Space!
  Muons (very heavy electrons)
    Most abundant particle in shower
    Deposits energy in matter in an even distributed manner
    Like throwing a baseball at a stack of pillows
    They don’t do much damage to you or electrical circuits
  Neutrons
    ~70per hour per square centimeter in Los Alamos
    Only “see” nuclei
    Most matter is nearly invisible to a neutron – just goes right through
    However, when it hits something, it hits it HARD!
  Radiation and you
    3.5 billion years of evolution has equipped you to repair yourself
    Computers aren’t as good at self-repair

## Slide 21: Impact of silent data corruption
No Fault-tolerance
Checkpoint/restart
Probability of incorrect results