## Slide 1: Performance analysis, Scalability and Isoefficiency, continued.
Laxmikant V. Kale

## Slide 2: Gauss-Jacobi Relaxation
while (maxError > Threshold) {
Re-apply Boundary conditions
maxError = 0;
for i = 0 to N-1 {
for j = 0 to N-1 {
B[i,j] = 0.2 * (A[i,j] + A[i,j-1] +
A[i,j+1] + A[i+1, j] + A[i-1,j]) ;
if (|B[i,j]- A[i,j]| > maxError)
maxError = |B[i,j]- A[i,j]|
}
}
swap B and A
}
Sequential Pseudocode:
Decomposition by:
Row
Blocks
Or Column

## Slide 4: Recap of steps
Outline: Express total work as a function of number of processors, to satisfy the condition that parallel efficiency is constant
Work: can be measured many different ways,
  but we will focus on total number of floating point operations, if you were to execute it sequentially
  Alternative: DRAM accesses (equivalently, level 3 cache misses)
Efficiency may decrease with additional processors for many reasons, but we will focus on communication costs
Algorithm may have other parameters, such as data array size N, but they should be expressed as a function of W
So: write the equation: communication-time = K* computation-time, and solve for W in terms of P
Make simplifications as necessary

## Slide 5: Isoefficiency of Jacobi Relaxation
Row decomposition
Computation per proc:
  A * N * (N/P)
Communication:
  16 * N
Comm-to-comp Ratio:
  (16 * P) / (A * N) = γ
Efficiency: 1 / (1 + γ)
Isoefficiency:
  Keep γ constant
  16P/(A.N) = γ, ie P/N = k
  problem-size W = N2, N = sqrt(W)
  P/sqrt(W) = k; W = (P/k)2
Notes: 5

## Slide 6: Simple Molecular Dynamics
Collection of [charged] atoms, with bonds
  Newtonian mechanics
  Thousands of atoms (1,000 - 500,000)
  1 femtosecond time-step, millions needed!
At each time-step
  Calculate forces on each atom
    Bonds: treated like springs
    Non-bonded: electrostatic and van der Waal’s
      Short-distance: every timestep
      Long range: ignore for this discussion
  Calculate velocities and advance positions

## Slide 7: The basic algorithm
Read atom info and iniialize
for I = 1, N
for J = 1, N
if (distance(A,i,j) < CutOff)
A[i].force = calculateForceBetween(A,i,j)
For i = 1,N
for each atom j that i is bonded to:
add forces on A[i] due to A[i]
// integrate
for I = 1, N
updatePositions(A,i)
A is an array of Atoms.
Each A[i] has:
double px,py,pz ; // positions
double vx, vy, vz; // velocities
double fx,fy,fz; // forces
double mass;
Aside: this ignores symmetry (Newton’s third law) which could be used to reduce the computation by half.. Its ok for now.

## Slide 8: Parallelization using Atom replication
Done in early codes,
  trying to extend their sequential code to run on parallel machines
Each processor keeps the entire array
Each processor calculates some subset of the interactions
  This may involve calculating forces on arbitrary sets of atoms
  So, need to add up all the forces and make them available to all processors (who then update the positions for all N)
  All-reduce with an array of size N takes time N.logP
    This is the communication cost

## Slide 9: Analysis of replicated data
Computation: for each atom, a constant number of atoms are within its cutoff radius
  Approx. 300 for typical simulations with 12 Angstrom cutoff
  with relatively uniform densities
  In any case, the number of interactions don’t increase with N
Computation time per processor: k.N/p
  (with some large k)
Communication: N. logP
Communication/Computation Ratio: (P log P)/k
  ! No N in the expression.. Just keeps increasing with P, with no scope for reducing it with a larger problem size

## Slide 10: Traditional Approaches: non isoefficient
Replicated Data:
  All atom coordinates stored on each processor
    Communication/Computation ratio: P log P
Partition the Atoms array across processors
  Nearby atoms may not be on the same processor
  C/C ratio: O(P)
Distribute force matrix to processors
  Matrix is sparse, non uniform,
  C/C Ratio: sqrt(P)

## Slide 11: Spatial Decomposition
Atoms distributed to cubes based on their location
Size of each cube
  Just a bit larger than cut-off radius
  Communicate only with neighbors
  Work: for each pair of neighbor objects
Communication to computation ratio: O(1)
However:
  Load imbalance
  Limited Parallelism