## Slide 1: Interconnect Topologies
Nikhil Jain

## Slide 2: Shared Memory
PE0
PE1
PEN
Memory
PE2
Is anyone in charge of a part of memory?
Is there a notion of relative proximity?
NO
No
May be

## Slide 3: Not entirely true!
PE0
PE1
PEN
Memory
PE2
Some part(s) of memory may be closer than others
What kind of network?
Network
Bus
Switch

## Slide 4: Distributed Memory Systems
PE0
Mem0
Others
PE1
Mem1
Others
PE2
Mem2
Others
PEN
MemN
Others
Locality of data is exposed
But beyond that…

## Slide 5: Programmer’s View
PE0
PE1
PEN
Rest of the System
PE2
How is the rest of the system connected?
Why do I care?
Mem0
Mem1
Mem2
MemN
Ring, Star, Butterfly, Mesh, Torus, Tree..
PERFORMANCE

## Slide 6: Commonly Discussed Network Topologies
Slide from a lecture by Prof Heath

## Slide 7: Commonly Discussed Network Topologies
Slide from a lecture by Prof Heath

## Slide 8: Commonly Discussed Network Topologies
Multi-tier all-to-all

## Slide 9: Basic Topology requirements
For things to work
  Must connect each processor to all others. i.e. it should be possible to send “messages” between any pair of processors
  Must allow for physically viable arrangements (try arranging a star for thousands of processors)
  The physically viable arrangement should be economically affordable

## Slide 10: Basic Topology requirements
For things to work well:
  Intermediate routing, if needed, should happen without interfering with computation on intermediate nodes.
  Reasonable path length between every pairs of processors
  Easy to calculate path from one processor to other
  More discussed later…

## Slide 11: Topology Basic definitions
Let the topology be represented by a Graph G(V,E) where V is the set of vertices - processors/routers and E is the edges - connections among them
degree: maximum number of edges incident on a vertex
distance between two vertices: number of edges (hops ) in shortest path between them
diameter: maximum distance between any pair of vertices
edge length : maximum physical length of any wire; may be constant or variable as number of processors varies
bandwidth

## Slide 12: How to Judge a Topology
degree: affects capability to communicate simultaneously
diameter: determines the maximum delay
average distance
link bandwidth: impacts how fast communication is done
bisection bandwidth
  Divide the set of processors in two equal partitions
  How much link bandwidth is available for data flow from one partition to the other? – Minimize it
  Important for global communication, congestion

## Slide 13: Fully Connected Network
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
What if everyone wants to send data to every one else?
Does this look like an overkill?
P-1
1
B.P.P/4
1
P(P-1)/2

## Slide 14: Chains
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
Single point of failure!
Asymmetric – not a good idea
1-2
P-1
B
P/3
P-1

## Slide 15: 2D Meshes (say P = k * k)
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
Asymmetric – not good!
Bisection bandwidth is decent: can be n-dimensional
2-4
2(k-1)
kB
2k/3
2k(k-1)

## Slide 16
Slide from a presentation by Prof. Dr.-Ing. Axel Hunger

## Slide 17: Are Hypercubes optimal? Moore Graphs
Moore bound: given degree d and diameter k, the largest number of nodes a graph can have is:
Conversely, given n vertices, and degree d, the best diameter we can hope for is: k = log(d-1)(n)
Given n = 1000, d = 10, k >= 4
A Moore graph has the maximum number of vertices possible among all graphs with maximum degree d and diameter k.

## Slide 18: Known Moore graphs
Peterson Graph: 10 vertices, degree = 3, diameter = 2.
Singleton graph: 50 vertices, degree = 7, diameter = 2
A 3rd graph might possibly exist, of degree 57!

## Slide 19: Why did Hypercubes Die?
Disadvantages of hypercube?
  Wire lengths? May span the entire machine
    Leads to reduced bandwidth per link, unless its optical
    Copper vs optical interconnects:
      Copper is cheaper but constrained by length
  Number of connections per node increases with the size of the machine
K-ary n-cube allows one to seek intermediate points between meshes and hypercubes.
  N-dimensional “hyper” cube, but number of processors along each dimension is k (instead of 2 of binary hypercube)

## Slide 20: Rings (k-ary 1-cube, or wrapped chain)
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
Why did I draw ring as a circle?
What if everyone wants to send data to every one else?
2
P/2
2B
P/4
P

## Slide 21: 2D Torus (k-ary 2-cube)
degree:
diameter:
average distance
total links/link bandwidth:
bisection bandwidth:
Bisection bandwidth is decent
But other issues, beyond the scope of this lecture
4
k-1
2kB
k/2
2k*k

## Slide 22: k-ary n-cube
P = k * k * k *…. Or P = k1 * k2 * k3 * ….
Degree = 2n
Diameter = n*k/2
Average Distance = n*k/4
Bisection Bandwidth = 2B*P/k

## Slide 23: Multi-tier Networks
Multi-tier all-to-all

## Slide 24: Switches and Indirect networks
node
switch
switch
switch
switch

## Slide 25
Slide from a presentation by Prof. Dr.-Ing. Axel Hunger

## Slide 26
Slide from a presentation by Prof. Dr.-Ing. Axel Hunger

## Slide 27: Butterfly
For P processors, log p ranks with p switches
Node(i,j) is connected to two nodes with rank i-1 – node(i-1,j) and node(i-1,m) where m is the integer found by flipping the ith most significant bit in binary representation of j
Rank 3 vertices can be processors/memory

## Slide 28: Butterfly
Routing is simple: follow the binary
0 means ship left;
1 means ship right.
diameter: log P
Average distance log P
bisection: P/2
What is not good?

## Slide 29: Omega networks

## Slide 30: Fat Tree/Clos Topology
a)
b)
c)
4-ary 1-tree
4-ary 2-tree
4-ary 3 tree

## Slide 31: Summary

## Slide 32: Things to explore
Which network suits which type of communication?
Find the networks used in modern machines – Mira, Blue Waters, Stampede, Tianhe, K computer.
How does one embed one topology in another topology?
How would you connect processors?